CS 447-002 Networks and Data Communications

Spring 2024

Quiz #6 on March 18, 2024 (SOLUTIONS)

Your Last Three Digits: ________________

(please do NOT write all of your student ID or your name)

Grade: ______

************************************************************************

- Define local area networks (“LANs”) by answering the following issues:

(a)	Primary purpose: for offering direct/physical connectivity to each host computer (connectivity to any computer networks, such as LANs, WANs, the Internet, and/or intranets)

(b)	Size: up to approximately 300 feet

(c)	Ownership: single ownership (individual owners, corporate, or organizations)

- Define internet (the Internet) by answering the following issues:

(a)	Primary purpose: for inter-connecting networks (primarily WANs) owned by long-distance carriers (i.e., ISPs)

(b)	Size: world-wide

(c)	Ownership: no single ownership (i.e., no one owns the Internet)

- What are “repeaters”?

Repeaters (including repeater hubs) are the network connection devices that “reform signals (distorted/partially corrupted signals are “restored”)” and forward the restored (cleaned up) signals to another (other) LAN(s) or host computer(s) to extend the size (length) of LANs or (network) cables.

- What is the primary advantage of “switch” (compared with “repeaters”)?

The primary advantages of switches are (any one of the followings):

- Switches do not broadcast, which eliminates unnecessary network traffic (“traffic localizer").  This property of switches prevents waste of network transmission bandwidth which may be wasted otherwise.

- Since switches can possibly set up multiple transmission paths inside of a switch, (network) transmission throughput at a switch is usually better (higher) than that of a repeater hub.

- Since switches will transmit (forward) network traffic (packets) only if its destination exists (if you are not a receiver, you will not see it), switches improve safety (security).

(5) What particular problem in CSMA does CSMA/CD solve and how?

CSMA/CD eliminates the time (wasted time) a transmitting host needs to wait for its timer to expire before the transmitting host computer can starts its retransmission when a packet collision occurs.

________________________________________________________________________

CS 447-002 Networks and Data Communications, Spring 2024, Quiz #6, March 18, 2024