CS447 – Networks and Data Communications

Spring 2024

Exercise Questions on January 23rd, 2024

EXERCISE #1:

- A 100-Mbps connection between A and B

- Packet size = 120 bytes

- Signal propagation delay is 20(s

What is the link-utilization, if stop-and-wait flow-control is used?

Should your work.

EXERCISE #2:

In the figure below, frames (packets) are generated at node A and sent to node C through node B.  Determine the sliding window size so that the buffer at node B will not overflow, based on the following conditions:

- The data rate between A and B is 100 Mbps (M = 106)

- The data rate between B and C is 200 Mbps

- The propagation delay is 20(s and 5(s for link A-B and B-C, respectively.

- The links are both full-duplex links.

- All data frames are 400 bits long; ACK messages are separate frames of negligible length (frame transmission delay = 0).

- For link A-B, sliding window flow control is used.

- For link B-C, stop-and-wait flow control is used.

- Assume no error.

_______________________________________________________________________

CS447, Exercise Question on January 23, 2024