## Slide 1
Performance Analyses (Link Utilization)
 For Stop-and-Wait ARQ
- Packet Error Rate (PER, 0.0 < ‘P’ < 1.0)
P = 0.15 (15% of the packets will be in some problem: 85 out of 100 packets will succeed)
Network Transmission Bandwidth Utilization (U) =
( +  + )

(TP + TT + TP)
TT
=
Link Utilization for “Stop-and-Wait Flow-Control”)
Link Utilization for “Stop-and-Wait ARQ”)
(1) If we transmit a total of 100 packets
(2) While P = 0.0
100 × (TP + TT + TP)
100 × TT
(TP + TT + TP)
TT
=
(1) If we transmit a total of 100 packets
(2) While P = 0.15
100 × (TP + TT + TP)
85 × TT
(TP + TT + TP)
(1 –P) × TT
=
How many packet(s) will be retransmitted for each
unsuccessful packet transmission under Stop-and-wait ARQ?
= 1 packet

## Slide 2
 For Selective-Reject ARQ
- Packet Error Rate (PER, 0.0 < ‘P’ < 1.0)
P = 0.15 (15% of the packets will be in some problem: 85 out of 100 packets will succeed)
Network Transmission Bandwidth Utilization (U) =
Link Utilization for “Sliding-Window Flow-Control”)
Link Utilization for “Stop-and-Wait ARQ”)
(1) If we transmit a total of 100 packets
(2) While P = 0.0
(1) If we transmit a total of 100 packets
(2) While P = 0.15
U = (N  TT)/(TT + (2  TP)) if (N  TT) < (TT + (2  TP))
U = 1.00 (= 100%) Otherwise (if (N  TT)  (TT + (2  TP)))
How many packet(s) will be retransmitted for each
unsuccessful packet transmission under selective-reject ARQ?
= 1 packet
U = (1-P) × (N  TT)/(TT + (2  TP)) if (N  TT) < (TT + (2  TP))
U = (1-P)×1.00 (= 85%) Otherwise (if (N  TT)  (TT + (2  TP)))

## Slide 3
 For GBN ARQ
- Packet Error Rate (PER, 0.0 < ‘P’ < 1.0)
P = 0.15 (15% of the packets will be in some problem: 85 out of 100 packets will succeed)
How many packet(s) will be retransmitted for each
unsuccessful packet transmission under GBN ARQ?
 1 packet (? packets)